After days of no success in regenerating the drierite by keeping it in the glassware drying oven, I went to the drierite website and discovered this:*The Importance of Temperature*The temperature at which DRIERITE desiccants are regenerated is crucial in restoring DRIERITE to its original condition. Absorbed moisture is water of hydration and is chemically bound to the calcium sulfate of DRIERITE. Temperatures in the range of 400¡ - 450¡ F are required to break these bonds and release absorbed moisture. Lower temperatures, regardless of heating time, will not regenerate DRIERITE unless applied under vacuum (26" Hg, 325¡ F or 28" Hg, 275¡ F). Care should be taken not to overheat DRIERITE Desiccants. High temperatures can alter the crystal structure and render the desiccants permanently inactive.Indeed, after I baked it for an hour at 425 it was good as new.- M-- Michael R. Markham, Ph.D.Department of Biological SciencesFlorida International UniversityMiami, FL  33199Phone: 305-348-0377     Fax: 305-348-1986